## Slide 1: Efficient Hardware Accelerator for Real-Time Facial Computing on Resource-Constrained Edge Devices
Name: P.A.P.S. Perera
Index: 23PG1-015
Supervisor: Eng. Kasun K. Herath
Co-Supervisor: Dr. Lasith Yasakethu
MSc in Embedded Systems and IC Design

## Slide 2: Introduction
Edge computing enables real-time processing on devices with limited resources. [3, 4, 6]
Facial computing tasks (e.g., recognition, detection) rely on Convolutional Neural Networks (CNNs). [ 8, 10, 11]
Challenges:
  High computational demands of CNNs.
  Limited processing power and memory in edge devices.
Objective: Design a hardware accelerator to optimize CNNs for edge devices.

## Slide 3: Research Problem
Problem:
Achieving real-time facial computing on resource-constrained devices is difficult due to:
  Slow processing speeds
  High power consumption
  Limited memory
Solution:
Custom FPGA-based hardware accelerator to speed up CNN computations.

## Slide 4: Research Objectives
Design and implement FPGA-based hardware accelerators for CNNs.
Optimize memory hierarchy and data transfer mechanisms.
Offload computational tasks from CPU to hardware.
Benchmark the performance of the hardware accelerator vs. software-based CNN processing.

## Slide 5: Literature Review Highlights
Deep learning on edge devices requires hardware accelerators (FPGA, GPU, etc.). [6, 8]
Existing solutions lack real-time performance on constrained devices.
FPGA: Ideal for parallel processing and optimizing computational tasks like CNN operations. [8, 10, 11]
Gap: In practical, Real-time facial computing on edge devices with CNN has not been fully explored between FPGA-based vs software with FPGA-Based systems.

## Slide 6: Methodology (conti..)
Design custom hardware accelerator (Net Engine IP).
Implement CNN layers for convolution and max-pooling.
Perform benchmarking:
  Compare accuracy and processing time for hardware and software based and pure software-based implementations.
Overview

## Slide 7: Methodology (conti..)
Architecture of the hardware accelerator includes:
  Net Engine IP for convolution and max-pooling operations.
    With 5 stage pipelining
  DMA controllers for efficient data transfer between memory and processing unit/ Programmable Logic unit.
  PL (Programmable Logic) for CNN operations.
Goal: Reduce latency, increase processing efficiency.
System Design

## Slide 8: Methodology (conti..)
Platform: PYNQ-Z2 development board (ZYNQ-7000 SoC).
Tools:
  Vivado 2023.2 for hardware design.
  Vitis 2023.2 for driver and software development.
Design focus: Efficient use of FPGA resources for CNN layers and data handling.
Hardware Setup
Time Measuring GPIOs

## Slide 9: Methodology (conti..)
System Design

## Slide 10: Methodology (conti..)
PL Implementation

## Slide 11: Methodology (conti..)
PS Implementation

## Slide 12: Methodology (conti..)
Proposed Network (PNet)

## Slide 13: Methodology (conti..)
Convolution Operation:
Loop through the image pixels.
Apply convolution kernel (3x3) over the input pixels.
Store the output.
Designed to work in parallel for faster execution with 5 stage pipeline.
Pseudocode
Max-Pooling Operation:
Loop through the image.
Apply max-pooling (3x3 window).
Store the maximum value in the output.
5 stage pipelining

## Slide 14: Result
Accuracy Evaluation (Respect to the software-based solution)
  Numerical Comparison
  Visual Comparison
  Entire Model Accuracy Comparison
Power Utilization
Timing Analysis

## Slide 15: Result (conti..)
Accuracy - Numerical Comparison
Channel | Correlation Coefficient | Chi-Square Statistic | Histogram Intersection
Channel 1 | 1.000 | 0.099 | 1.000
Channel 2 | 1.000 | 0.032 | 0.999
Channel 3 | 1.000 | 0.012 | 1.000
Channel 4 | 1.000 | 0.011 | 1.000
Channel 5 | 1.000 | 0.004 | 1.000
Channel 6 | 1.000 | 0.078 | 0.999
Channel 7 | 1.000 | 0.074 | 0.999
Channel 8 | 1.000 | 0.029 | 0.999
Channel 9 | 1.000 | 0.039 | 1.000
Channel 10 | 1.000 | 0.039 | 0.999

## Slide 16: Result (conti..)
Accuracy - Visual Comparison
Software Only
Software with Net Engine
Software Only
Software with Net Engine

## Slide 17: Result (conti..)
Power Consumption
Dynamic Power | Clocks | 0.014w
 | Signals | 0.004w
 | Logic | 0.003w
 | BRAM | 0.001w
 | I/O | 0.003w
 | PS7 | 1.564w
Device Static Power |  | 0.145w
Total Power |  | 1.735w

## Slide 18: Result (conti..)
Timing Analysis
Chart: Model Processing Time
| 1 | 0.95 | 0.9 | 0.85
Without Net Engine | 1.5988 | 1.4032 | 1.2713 | 1.0973
With Net Engine | 0.28663 | 0.25728 | 0.23699 | 0.21136
Chart: CNN Layer Processing Time
| 1 | 0.95 | 0.9 | 0.85
Without Net Engine | 0.27536 | 0.24796 | 0.22203 | 0.1975
With Net Engine | 0.04205 | 0.038238 | 0.034629 | 0.031173

## Slide 19: Result (conti..)
Timing Analysis (Conti..)
Chart: Channel Processing Time
| 1 | 0.95 | 0.9 | 0.85
Without Net Engine | 0.027537 | 0.024798 | 0.022202 | 0.01975
With Net Engine | 0.0042133 | 0.0038212 | 0.0034723 | 0.0031231
Chart: Single Frame Processing Time
| 1 | 0.95 | 0.9 | 0.85
Without Net Engine | 0.008408 | 0.0075728 | 0.0067814 | 0.0060326
With Net Engine | 0.00066135 | 0.00060083 | 0.00055769 | 0.00050665

## Slide 20: Discussion
Performance gains:
  Significant reduction in processing time (82% reduction).
  High accuracy in hardware replication of CNN.
Energy efficiency: Suitable for real-time edge AI applications.
Scalability: Can be adapted for other CNN-based tasks on embedded systems.

## Slide 21: Conclusion
Achieved objectives: Efficient real-time facial computing on constrained devices respect to the pure software based solution.
Net Engine:
  Improves processing time and power efficiency.
  Maintains high accuracy.
Contribution: Provides a practical solution for deploying CNNs on edge AI devices.

## Slide 22: Future Work
Explore scaling the Net Engine for more complex CNNs.
Optimize memory usage further to handle larger networks.
Optimized CNN implementation on Software Side
Extend the solution to other real-time applications (e.g., gesture recognition).

## Slide 23: References
A. B S, S. R. (2022). "NC-Emotions: Neuromorphic hardware accelerator design for facial emotion recognition,". 29th IEEE International Conference on Electronics, Circuits, and Systems (ICECS), 1-4. doi:Glasgow, United Kingdom
A. Baobaid, M. M. (2022). "Hardware Accelerators for Real-Time Face Recognition: A Survey,". IEEE Access, 10, 83723-83739. doi:10.1109/ACCESS.2022.3194915
al., A. M. (2019). "Deep Learning for Edge Computing: Current Trends, Cross-Layer Optimizations, and Open Research Challenges,". 2019 IEEE Computer Society Annual Symposium on VLSI (ISVLSI), 553-559. doi:10.1109/ISVLSI.2019.00105
al., X. L. (2022, Feb). "Collaborative Edge Computing With FPGA-Based CNN Accelerators for Energy-Efficient and Time-Aware Face Tracking System,". IEEE Transactions on Computational Social Systems, 9, 252-266. doi:10.1109/TCSS.2021.3059318

## Slide 24: References (Conti..)
Rao, B. S. (2021). "Binary neural network based real time emotion detection on an edge computing device to detect passenger anomaly,". 2021 34th International Conference on VLSI Design and 2021 20th International Conference on Embedded Systems (VLSID), 175-180. doi:10.1109/VLSID51830.2021.00035
S. Liu, L. L. (2019, Aug). "Edge Computing for Autonomous Driving: Opportunities and Challenges,". Proceedings of the IEEE, 107, 1697-1716. doi:10.1109/JPROC.2019.2915983
Talib, M. M. (2021, Feb). A systematic literature review on hardware implementation of artificial intelligence algorithms. J Supercomput 77, 1897–1938. doi:10.1007/s11227-020-03325-8
Dasgupta, F. S. (2017). "Automated flow for compressing convolution neural networks for efficient edge-computation with FPGA". California: MLPCD workshop, NIPS. doi:https://doi.org/10.48550/arXiv.1712.06272

## Slide 25: References (Conti..)
Xue Lv, M. S. (2021). Application of Face Recognition Method Under Deep Learning Algorithm in Embedded Systems. Microprocessors and Microsystems. doi:10.1016/j.micpro.2021.104034
Y. S. Mounika, B. B. (2022). "FPGA BASED HARDWARE ACCELERATOR FOR CONVOLUTION NEURAL NETWORK,". 2022 International Conference on Recent Trends in Microelectronics, Automation, Computing and Communications Systems (ICMACC), 260-264. doi:10.1109/ICMACC54824.2022.10093648.
Yu, C. F. (2019). "FPGA-based Power Efficient Face Detection for Mobile Robots,". 2019 IEEE International Conference on Robotics and Biomimetics (ROBIO), 467-473. doi:10.1109/ROBIO49542.2019.8961745

## Slide 26: Thank You
Any Questions?
GitHub Repo:
https://github.com/Pankaja-Suganda/Net-Engine-FPGA-With-Software.git

## Slide 27: Register File
Register Name | Description | Offset
Status Registers |  | 
NET_ENGINE_STATUS_REG_1 | Status information | 0x00
NET_ENGINE_STATUS_REG_2 | Status information | 0x04
NET_ENGINE_STATUS_REG_3 | Status information | 0x08
NET_ENGINE_STATUS_REG_4 | Status information | 0x0C
NET_ENGINE_STATUS_REG_5 | Status information | 0x10
NET_ENGINE_STATUS_REG_6 | Status information | 0x14
Configuration Registers |  | 
NET_ENGINE_CONFIG_REG_1 | Select convolution / max-pooling Operation | 0x18
NET_ENGINE_CONFIG_REG_2 | Input Row Length | 0x1C
NET_ENGINE_CONFIG_REG_3 | Net Engine Enable/Disable | 0x20
NET_ENGINE_CONFIG_REG_4 | Reserved | 0x24
Kernel and Bias Registers |  | 
NET_ENGINE_BIAS_REG | Bias values for convolution operations | 0x28
NET_ENGINE_KERNEL_REG_1 | Kernel weights for convolution operations | 0x2C
NET_ENGINE_KERNEL_REG_2 | Kernel weights for convolution operations | 0x30
NET_ENGINE_KERNEL_REG_3 | Kernel weights for convolution operations | 0x34
NET_ENGINE_KERNEL_REG_4 | Kernel weights for convolution operations | 0x38
NET_ENGINE_KERNEL_REG_5 | Kernel weights for convolution operations | 0x3C
NET_ENGINE_KERNEL_REG_6 | Kernel weights for convolution operations | 0x40
NET_ENGINE_KERNEL_REG_7 | Kernel weights for convolution operations | 0x44
NET_ENGINE_KERNEL_REG_8 | Kernel weights for convolution operations | 0x48
NET_ENGINE_KERNEL_REG_9 | Kernel weights for convolution operations | 0x4C

## Slide 28: Convolution Implementation

## Slide 29: Maxpooling Implementation

## Slide 30: Net-Engine Driver Implementation

## Slide 31: Neural Network Implementation

## Slide 32: Time Measurement

## Slide 33: Time Measurement